## Slide 1: Subthreshold Dual Mode Logic
Author: A. Kaizerman, S. Fisher, and A. Fish
Presenter: He, Yousef

## Slide 2: Motivation
Power consumption is the primary focus of attention in VLSI digital design today
Subthreshold
Problems?
Performance Degradation
High sensitivity to PVT variation

## Slide 3: CMOS vs Dynamic
CMOS
Dynamic
The most common logic design family used for subthreshold today is CMOS
The advantage of CMOS is low power
The disadvantage of CMOS is low performance compare to other logic families
The advantage of Dynamic logic is high performance
The disadvantage of Dynamic logic is high power

## Slide 4: Domino
http://www.cerc.utexas.edu/~jaa/vlsi/lectures/12-1.pdf
1.5-2X faster than static CMOS
Low Robustness

## Slide 5: DML
Dual mode logic (DML): Can be operated in static CMOS-like mode and dynamic mode
DML shows high immunity to process variations
“Subthreshold Dual Mode Logic”, A. Kaizerman, S. Fisher, A. Fish

## Slide 6: Contributions
This work:
Demonstrates the Dual Mode Logic structure
Demonstrates the energy savings of static DML compare to CMOS
Demonstrates the speedup of dynamic DML compare to CMOS
Demonstrates the Robustness to process variation of DML compare to CMOS

## Slide 7: Outline
Speed
Energy
Robustness – SNM
Robustness – delay
Logic level (LL) Analysis
Conclusion

## Slide 8: Speed
The dynamic DML gates with an average of an order of magnitude have higher-frequency than CMOS
The speed of dynamic DML is slightly lower than dynamic logic, but the robustness of DML is better than dynamic logic
“Subthreshold Dual Mode Logic”, A. Kaizerman, S. Fisher, A. Fish

## Slide 9: Outline
Speed
Energy
Robustness – SNM
Robustness – delay
Logic level (LL) Analysis
Conclusion

## Slide 10: Energy
The DML static mode demonstrated a lowest energy consumption, on average, 2.2× less than CMOS and 5× less than domino
“Subthreshold Dual Mode Logic”, A. Kaizerman, S. Fisher, A. Fish

## Slide 11: Outline
Speed
Energy
Robustness – SNM
Robustness – delay
Logic level (LL) Analysis
Conclusion

## Slide 12: Robustness-SNM
DML has smaller average SNM compare to CMOS
DML has larger sigma/mu of SNM compare to CMOS
“Subthreshold Dual Mode Logic”, A. Kaizerman, S. Fisher, A. Fish
 | mu | Sigma/mu
CMOS | 77m | 0.1
DML | 52m | 0.22

## Slide 13: Outline
Speed
Energy
Robustness – SNM
Robustness – delay
Logic level (LL) Analysis
Conclusion

## Slide 14: Robustness-Delay
CMOS has the lowest delay robustness to process variation, but DML is just slightly worse than CMOS, much better than Dominal
“Subthreshold Dual Mode Logic”, A. Kaizerman, S. Fisher, A. Fish
 | Sigma/mu
CMOS | 0.42
DML (D) | 0.55
DML (S) | 0.55
Domino | 1.08

## Slide 15: Outline
Speed
Energy
Robustness – SNM
Robustness – delay
Logic level (LL) Analysis
Conclusion

## Slide 16: Robustness-Logic Level
Domino has unclear logic level at logic 1, DML can solve this problem
“Subthreshold Dual Mode Logic”, A. Kaizerman, S. Fisher, A. Fish

## Slide 17: Outline
Speed
Energy
Robustness – SNM
Robustness – delay
Logic level (LL) Analysis
Conclusion

## Slide 18: Conclusion
This paper:
presented a novel family DML
showed that the DML dynamic mode presented an average 10× speed improvement as compared to CMOS, and improved robustness as compared to a standard dynamic logic
demonstrated the lowest energy dissipation (DML static mode): 2.2× less than CMOS on average, and 5× less than the domino.

## Slide 19: criticism
The advantage of subthreshold is high energy efficiency. It is not clear why they want to achieve high performance in subthreshold region
No E-D curve to show a comprehensive comparison
The robustness of DML is worse than CMOS showed in this paper. However, the robustness of CMOS itself is not good in subthreshold region
Bad consistency between footers

## Slide 20
Thank you!
Questions?